## Slide 1
MiX Vision AI
Product Information Guide

## Slide 2
Video and Fleet Management Today
Notes: Video has become a foundation feature of telematics/fleet management solutions
Its introduction and diffusion is analogous to GPS positioning in the early days of telematics
Numerous traditional competitors have video-based offerings
New market entrants use video as the core of their offering
OEM’s are starting to embed video capabilities into their products, starting with ADAS features
Regulation is also starting to drive diffusion of video-based solutions e.g. London
Focal areas include;
  Driver monitoring and in-vehicle alerts e.g. distracted driving, fatigue
  Driver performance and coaching
  Live streaming
  Accident reconstruction and automated insurance claim handling
  After-market ADAS – forward collision warning, lane departure etc …

## Slide 3
The Future
The artificial intelligence (AI) algorithms are probabilistic in nature. While extensive testing has been done to ensure their reliability, there is no guarantee that they will be 100% accurate. ​
Notes: Video adoption drives data growth
This will also see the emergence of other market participants to compete with Telematics Service Providers
Video data is being used to support the development of AI-based autonomous vehicles
Transition from “video focused on people” to “machine vision” applications
Sensing of the external environment raising situational awareness and providing further new insights

## Slide 4
How will MiX Vision AI benefit Fleet Managers?
Reduce risky driving behaviour through AI & ADAS generated in cab alerts
Immediate supervisor insight into risky driver behavior
Detecting and acting on fatigue (for driver and passenger safety)
Improve driver coaching effectiveness
Reduce incident-related costs & liability
Improve incident investigation efficiency
Lower risk-related insurance overheads
Improve driver retention through visible investment in driver-focused duty-of-care technologies
Notes: Fleet Managers
  Reduce risky driving behaviour
  Improve operational efficiency - reduce downtime associated with risky driving behaviour and incidents
  Reduce incident-related costs - lost productivity and vehicle-related
  Improve effectiveness/efficiency of driver coaching efforts from driver managers
  Improve effectiveness and efficiency of incident investigation
  Reduce incident-related liability
  Lower risk-related insurance overheads
  Improve driver retention through visible investment in driver-focused duty-of-care technologies

## Slide 5
How will MiX Vision AI benefit drivers?
More contextual information related to driving performance
Feel engaged in the performance coaching process
Become a better driver
Feel supported by company when it comes to blame for incidents
Notes: Drivers
  More contextual information related to driving performance
  Feel engaged in the performance coaching process
  Become a better driver
  Feel supported by company when it comes to blame for incidents

## Slide 6
Driver Performance Management
Event-based video
(Video end of trip)
AI/ADAS event video
(Video in trip)

## Slide 7
Flexible Driver Scoring
OBC-detected events
Harsh braking
Harsh acceleration
Speeding
OBC-detected events
Harsh braking
Harsh acceleration
Speeding
+
Machine vision-detected events
Fatigue
Phone use
Distraction
Seat belt
Current Driver Scorecard
Flexible Driver Scorecard
Lane departure
Forward collision
Following distance
Measure of risky driving behavior
Measure of driving performance

## Slide 8
MiX Vision AI
Detect, Alert & Provide Insights on in-cab activities in MiX Fleet Manager & MyMiX
C6D AI
Forward-facing ADAS camera: Max 1080P @ 20FPS
  Lane departure warning
  Forward collision warning
  Following distance warning
Driver-facing DSM camera: Max 960P @ 20FPS
  Fatigue warning
  Phone use warning
  Distraction warning
  Seat belt warning
OBC-triggered events with road and in-cab video
  Harsh braking
  Harsh acceleration
  Speeding
  Impact detection
  Rollover detection
Machine vision
Machine vision
All events have in-cab, real-time driver coaching feedback via the camera display screen or the OBC buzzer
MiX Vision AI

## Slide 9
MiX Vision AI: Parts Overview
A-Pillar Mount
Dash Mount
Function: In-cab view
This camera provides a view from inside the vehicle.
Contains mic for audio recording. No AI capability on this camera, just a static camera
Function: Driver Fatigue
The DSM camera is used for Driver Fatigue detection (AI events).
Two variants are available to order, both have mic.
Dash Mount and A-Pillar
Function: Visual Feedback
The In-cab coach provides a visual feedback for the driver on the event triggers (ADAS/AI).
Function: ADAS/Road Facing
This is the main unit which contains the Cat4 LTE modem and Road Facing camera for ADAS events.
This unit contains mic and speaker. Speaker is used for audible alerts.
Road-facing Camera
In-cab Camera *
Driver Camera *
AI Driving Coach *

## Slide 10
Feature Comparison
Feature | MiX Vision Gen 1 | MiX Vision Next Gen
Event-based video clips | Yes (8 sec) | Yes (8 sec)
Driver snapshot | Yes | Yes
Videos viewable in Historical Tracking, Trip Timeline & MiX Insight Reports | Yes | Yes
Custom clips (Video Tacho) | Yes (72hrs) | Yes (72hrs)
Downloading clips (2,5mins) | Yes | Yes
HD capability | Request High Res Video | Request High Res Video (Future)
Live Streaming | Yes | Yes (Future)
Additional cameras | Yes | Yes (Future –different hardware model)
Video Overlay | Date/time Speed/RPM | GPS speed UTC Date/time
Video availability through MiX Integrate | Yes | Yes
Passive ADAS | No | Yes
Driver monitoring AI events | No | Yes

## Slide 11
Hardware Comparison
Feature | MiX Vision MVR2214 | MiX Vision MVR3322 | MiX Vision Streamax C6D AI
Road-facing Camera | 480p | 1080p 10fps 3Mbps max | 1080p 30fps 6Mbps max (4mm lens)
In-Cab Camera | 480p | 1080p 10fps 3Mbps max, IR | 720p 10fps 6Mbps max (2.3mm lens), IR
Max number of cameras | 4 | 2 | 2
GPS | No | No | Yes, used for AI events
Accelerometer | No | No | Yes - not used
CAN | No | No | Yes - not used
LTE with 3G | 3G only | Yes | Yes Quectel EC25 LTE-Cat4 with 3G fall back
Partitions | 3 (configurable) | 3 (configurable) | 1
Timing of event video (default) | 4s before event | 4s before event | 4s before event
Live streaming | Yes | Yes | Yes (future)
Wifi support | No | No | Yes - not used
Serial Port | RS-232 | RS-232 | 1 x RS-232, 1 x RS-485 - not used
Speaker | No | No | Built-in
Microphone | Optional | Optional | Built-in – not used
Overlay contents | Time (UTC + offset) | Time (UTC + offset) | Time (UTC)
 | RPM | RPM | Speed (GPS)
 | Speed (OBC) | Speed (OBC) | 
 | MiX Logo | MiX Logo | 
Max SD card capacity | 128 GB | 128 GB | 2 x 64 GB
Analog inputs | 0 | 0 | 4 (2 buttons, 2 sensors)- not used
Frequency inputs | 0 | 0 | 1 (speed) – not used

## Slide 12
Solution Video
Click play to view

## Slide 13
Cathexis gap & solutions
No HD video request – future development
Only 2 cameras - future development to integrate 4 camera hardware
No Live Streaming - future development
More comprehensive diagnostics and reporting – continuous improvement will be provided by Streamax
No private APN – can be supported on request
No pinned SIM – not supported & no plans
No export for combined camera clips - not supported & no plans
MiX Insight Reports icon for road facing camera only - future development
Request clip > or < 2.5min - not supported & no plans

## Slide 14
Release Phases and Roadmap

## Slide 15
Next Generation Video Roadmap
MiX Vision
Next Gen Hardware
Flexible Driver Scoring
Video Evidence-based Coaching
Dashboards, Analytics & Insights
Q1 2021
TBC
Live Streaming

## Slide 16
Development Phases
Phase 2: Incorporating machine vision events (AI) end of April 21
    Driver monitoring event detection
    ADAS event detection
Phase 3: Support Camera 3&4 [TBC]
    Requires integration of other video unit models into existing video communication service
Phase 4: Live video streaming [TBC]
Planned features:
    DSM & HD footage download
    Fatigue event accumulation and escalation
    Real time OBC event videos
    Standalone Streamax device
    Motorbike detection (Streamax)
    Flight mode (Streamax)
    Improved diagnostics (Streamax)
    Firmware maintenance platform improvements – user permissions, etc. (Streamax)

## Slide 17
Release Phases
  Pre-launch phase for the next generation of MiX Vision [Jan –Feb]
    Installation & Support upskilling for AI/ADAS capable installations
    Understanding the AI and ADAS features – expected behaviour of a probability-based solution
  US marketing launch [Feb 21]
    Online marketing campaign
  Optional pre-installation phase – “AI/ADAS ready” installations [Mar 21]
    With sufficient regional installation & support upskilling
  Market release of Machine Vision features in MiX Fleet Manager [end of Apr 21]
    Machine Vision Events and Alerts in MiX Fleet Manager
    Machine Vision Events (& OBC events) in MiX Custom Scoring

## Slide 18
Software Setup

## Slide 19
New Standalone Peripheral type
The Streamax C6D-AI device can be connected on the Mobile device template
  It is connected to the SP line which is the connection for the new Standalone peripheral type
  This type indicates that there is no direct communication between the camera unit and the OBC
Note: Only the MiX4000, MiX6000, MiX 6000LTE and FM are supported

## Slide 20
Commissioning a Standalone peripheral
When an asset is added to a Configuration group with a connected C6D-AI peripheral, the details appear on the asset's Mobile device settings tab:
  The C6D-AI 10-digit serial number can be entered in the input box. This number is printed on the label of the C6D-AI device.
  Upon saving this information the device is set to commissioned in MiX Fleet Manager and events that are configured to record video in the event template will then have video associated.
After commissioning the device, it will no longer be possible to edit the serial number, but the device can be changed or removed

## Slide 21
Mobile Device Generated Event Configuration
To record a video on a mobile device generated event in the event template, select the “Record video” option under “Record” on the Event configuration page
This is only available on Detailed and Notification events
The event needs to be compiled and uploaded to the OBC’s configuration as it is mobile device generated
When the trip is processed the video footage is retrieved from the C6D-AI server for the date and time that the event occurred and is then associated to the event in MiX Fleet Manager

## Slide 22
AI Generated DSM & ADAS Event Configuration
The Streamax AI events are managed like all events in MiX Fleet Manager when the C6D-AI is connected to the SP line:
  These events are a new type – MiX Vision
  They can be configured at library level, template level and asset level
  Changes made at asset level will black flag the asset but the configuration will not be dirtied
When these events are triggered during a trip, they are sent in real time to MiX Fleet Manager
Note: the artificial intelligence (AI) algorithms that are used to detect these events are probabilistic in nature. While extensive testing has been done to ensure their reliability, there is no guarantee that they will be 100% accurate.

## Slide 23
Video Availability in MiX Fleet Manager

## Slide 24
Viewing Video Events – Historical Tracking​
Trip List​
View video events alongside vehicle information ​
Click on the video icon in the trip list to open the video player​
Map​
You can plot the trail on the map and click on the video icon to open the video player​
​
Video Player​
The video player displays videos based on the number of cameras connected​
At the top of the player is the event information linked to the video​
There is a “Full Screen” option in the bottom right corner of each individual clip​
You have the option to play clips individually or together​
​
Notes​
There is no HD video option on the C6D-AI
Due to different resolutions the video sizes may be different

## Slide 25
Viewing Video Events – Trip Timeline​
Trip Timeline​
Video events are displayed at the bottom of the screen along with all other events​
They have a video camera icon to distinguish them from other events​
The icon is clickable and opens the video player​
​
Video Player​
The video player displays videos based on the number of cameras connected​
At the top of the player is the event information linked to the video​
There is a “Full Screen” option in the bottom right corner of each individual clip​
You have the option to play clips individually or together​
Notes
There is no HD video option on the C6D-AI
Due to different resolutions the video sizes may be different

## Slide 26
Live Tracking, Info Hub & Notifications
Live Tracking & Info Hub
Active AI & ADAS events will be available in the Live Tracking & Info Hub
Active AI & ADAS videos can be viewed by selecting the event icon
Active AI & ADAS videos will be available within 5 mins of occurrence
Active Event Notifications
Active AI & ADAS event video will be accessible from a link in email notifications
Videos will be available within 5 mins of occurrence
SMS and Push Notifications can be set up for active AI & ADAS events, but no video will be available from the notification

## Slide 27
Requesting Custom Clips
A custom clip can be requested from the Trip Timeline
  Click on the downward actions arrow to the right of the Timeline
  Select Download video
  Select the time period that you would like to download video for
  Select which cameras you want to download video for
  Select Submit
  The tacho block for that time period will now be highlighted in orange and will have a video icon once the video is available
  You will receive an email notification when the request has been successful and can then view the clip from the Timeline
  Custom clips are 2:30 minutes long

## Slide 28
Driver Snapshot
The ‘Record trip driver picture” event is a default event that is triggered at the start of the trip
The event takes a snapshot image using the In-cab facing camera
The image can be viewed from Historical Tracking or Trip Timeline by clicking on the camera icon
The Driver snapshot info modal will open which shows information about the asset, driver, and trip
Conditions for driver picture to be triggered:
  Asset must be In Trip
  There must be video recorded and available for that time
  The DVR Ignition On Timer must be > 120 seconds (2 minutes)
  The speed must be more than the configured moving speed

## Slide 29
Insight Reports – Detailed Event Report
Videos can be downloaded from the Detailed Event Report
The “Visual Media” column needs to be selected under “Show columns” in the reporting wizard
When an icon is displayed in this column it means a video clip is available
Click on the icon to download the video
This functionality is only available in the online report

## Slide 30
Insight Reports – Driver Behaviour Report
The Driver Behavior Report shows a monthly or weekly trend of drivers’ RAG scores
Drill through to specific events that contribute to the score
When an icon is displayed in the “Visual Media” column it means a video clip is available
Click on the icon to download the video
Video aids in debriefing a driver for erratic driving practices

## Slide 31
Data Usage Warnings
Data usage warnings can be configured at an organizational and a per asset level:
  Monthly data usage thresholds can be set for both
  When data usage is within 20% of the threshold values a 1st warning email will be sent
  When data usage reaches the threshold a 2nd email will be sent
  The emails will be sent to the specified list of contacts

## Slide 32
MiX Integrate
Event based videos are available through MiX Integrate

## Slide 33
MiX Vision Events

## Slide 34
Driver Alerts
Speed is GPS velocity from the unit and not connected to your vehicle data
Machine vision algorithms are not active at low speeds
  For practical reasons e.g. driving in carparks, yards or transiting intersections
  Become active at 30km/hr [18mph] except for lane departure which becomes active at 55km/hr [34mph]
Standard Alert
Beep + voice message
Voice can be turned off – only recommended if the AI Driving Coach display is installed
Optional Alert
In-cab Coach
Speed thresholds for algorithm activation can be changed during installation in order to meet customer needs in special use cases e.g. metro bus and heavy vehicles operating in large processing plants

## Slide 35
OBC Events Based Videos
Your MiX4000 / MiX 6000 events can also record video (ensure record video enabled)
  Events will appear live in infohub if active
  Event video: Takes anywhere from 5min to 15min to upload after Ignition is switched off.
  Tacho video: Takes anywhere from 5min to 15min to obtain when IGN is ON.
  Only Road and In-Cab camera video will be available on MFM, not Driver Camera
  Video download will only happen after trip has ended

## Slide 36
ADAS Events
ADAS events are created as system events in the event library and do not have a duration but do record position
These events are triggered by the camera (not by the OBC) and are therefore active events
Because these events are active, they are also available in Info Hub, Live tracking and Event notifications
The following ADAS events are available:
  Lane Departure Warning (advisable when connected to turn signal)
  Forward Collision Warning
  Following Distance Monitoring
Note: the artificial intelligence (AI) algorithms that are used to detect the ADAS events are probabilistic in nature. While extensive testing has been done to ensure their reliability, there is no guarantee that they will be 100% accurate.
Following Distance Monitor
Forward Collision Warning
Lane Departure
Lane Departure
Indicate Following Distance

## Slide 37
ADAS Events Functionality
Following Distance Monitor
Active from ≥ 30km/h [18mph]
Trigger:
  Unsafe distance to front vehicle.
  The distance between the vehicle and front vehicle/vehicle absolute speed≤0.6S
Forward Collision Warning
Active from ≥ 30km/h [18mph]
Trigger:
  Risk of crashing into front vehicle
  The collision less than safe threshold value(relative vehicle distance/relative vehicle speed<2.7s)
Vehicle Detected Icon
Following distance estimate in seconds

## Slide 38
ADAS Events Functionality
Lane Departure Warning
Active from ≥ 55km/h [34mph]
Trigger:
  Front wheel about to cross the line without indicators
  Indicators needs to be on for at least 3 seconds
  Indicators needs to be wired to Analogue inputs

## Slide 39
DSM (Driver Status Monitor) Events
DSM events are created as system events in the event library and do not have a duration but do record position
These events are triggered by the camera and are therefore active events
Because these events are active, they are also available in Info Hub, Live tracking and Event notifications
The following DSM events are available:
  Driver Fatigue (eyes closed)
  Smoking
  Phone Use
  No Driver
  Yawning Detect
  Distracted Driver (looking up or down only)
  Seatbelt Detection (left hand drive only)
Note: the artificial intelligence (AI) algorithms that are used to detect the DSM events are probabilistic in nature. While extensive testing has been done to ensure their reliability, there is no guarantee that they will be 100% accurate.
Distracted Driver
Fatigue Warning
No Driver Detected
No Smoking
No Phone
Driver AI

## Slide 40
AI Events - Functionality
Driver Fatigue & Yawning
Active from ≥ 30km/h [18mph]
Trigger:
  Driver Yawns for 2 consecutive seconds
  Driver’s eyes closed for 2 consecutive seconds
  Blink frequently
Driver Distracted
Active from ≥ 30km/h [18mph]
Trigger:
  Driver looks up/down for 4 consecutive seconds

## Slide 41
AI Events - Functionality
Phone Detected
Active from ≥ 30km/h [18mph]
Trigger:
  Phone to your ear for 5 seconds
Seatbelt not Detected
Active from ≥ 30km/h [18mph]
Trigger:
  Not detecting Seatbelt for 4 seconds

## Slide 42
AI Events - Functionality
Smoking
Active from ≥ 30km/h [18mph]
Trigger:
  Smoking or gesture of smoking, also detects cigarette
No Driver
Active from ≥ 30km/h [18mph]
Trigger:
  DSM Camera covered
  Driver can be detected

## Slide 43
Diagnostic Events
The following diagnostic events can be monitored
  Video loss
  Motion detection
  Storage exception
  Low voltage
  Ignition
  lllegal shutdown

## Slide 44
In-Cab Hardware Setup & Installation

## Slide 45
Installation Positions
DSM Cameras
Only 1 can be installed, so you need to determine what is best for the vehicle.
Dash Mount is installed inform of the driver on the dash.
A-Pillar Mount is installed on the A-frame pillar of the vehicle to the side of the driver.
A-Pillar Mount
Dash Mount
Installation guides on MLC

## Slide 46
Functions
Road-facing Camera
In-Cab Camera
Function: In-Cab view
This Camera provide a view from inside the vehicle.
Contains mic for audio recording. No AI capability on this camera, just a static camera
Function: ADAS/Road Facing
This is the main unit which contains the Cat4 LTE modem and Road Facing Camera for ADAS events.
This unit contains mic and speaker. Speaker is used for audible alerts.

## Slide 47
Functions
A-Pillar Mount
Dash Mount
Driver Camera
AI Driving Coach
Function: Driver Fatigue
The DSM Camera are used for Driver Fatigue detection (AI events).
Two variants are available to order, both have mic. Dash Mount (Landscape) and A-Pillar (Portrait)
Function: Visual Feedback
The In-cab coach provide a visual feedback for the driver on the event (ADAS/AI) triggers.
Distracted Driver
Fatigue Warning
No Driver Detected
No Smoking
No Phone
Following Distance Monitor
Forward Collision Warning
Lane Departure
Lane Departure
Indicate Following Distance
ADAS
Driver AI

## Slide 48
Part IDs*
* All orders to be placed on CSO and will be shipped direct from the factory to the RSO
** 128 GB SD-Card is recommended
Section​​ | Part Number​​ | Product Name​​ | Description​​
Main Unit​​ | U0057MT​​ | MiX Vision C6D-AI (EU)​​ | C6D-AI with 4G module (EC25-EC - EMEA)​​
 |  |  | High Precision GPS, Wi-Fi Module, Built-in Speaker​​
 |  |  | Built-in ADAS Camera (for road view) ​​
 | U0058MT​​ | MiX Vision C6D-AI (US)​​ | C6D-AI with 4G module (EC25-AF - North America)​​
 |  |  | High Precision GPS, Wi-Fi Module, Built-in Speaker​​
 |  |  | Built-in ADAS Camera (for road view)​​
 | U0059MT​​ | MiX Vision C6D-AI (AU/BR)​​ | C6D-AI with 4G module (EC25-AU - Latam & Australia)​​
 |  |  | High Precision GPS, Wi-Fi Module, Built-in Speaker​​
 |  |  | Built-in ADAS Camera (for road view)​​
SD Card Options​ | A0054MT ​ | 64 GB SD-Card​ | 64GB Class 10 Industrial SD-Card (2 required per unit) ​
 | A0055MT ​ | 128 GB SD-Card**​ | 128GB Class 10 Industrial SD-Card (2 required per unit) ​
 | A0056MT ​ | 256 GB SD-Card​ | 256GB Class 10 Industrial SD-Card (2 required per unit) ​
In-Cab Camera​​ | P0029MT​​ | In-Cab Camera​​ | 720P SVTIP- 836C26 (in-cab monitor camera)​​
DSM Cameras​​ | P0026MT​​ | DSM Dash Mount Camera​​ | 960P SVT-DSM-L (Dash Mount DSM Camera)​​
 | P0027MT​​ | DSM A-Pillar Mount Camera​​ | 960P SVT-CL29M (A-Pillar Mount DSM Camera)​​
R-Watch​​ | P0028MT​​ | R-Watch​​ | R-Watch is a small colour display providing visual alerts to the driver ​​

## Slide 49
Data Usage Estimates
The MiX Vision AI makes use of Main Stream or Sub Stream video files. The Sub Stream is used for events and the Custom clips.
Event Video and Custom Clip will download InCab and Road Camera. This will result in 2 files per action.
Video size is based on transfer rate of 4.9MB/min or 83KB/sec for each camera.
Expected data usage is 494MB per month for 8 second duration videos and 12 events per day.
Live Streaming estimated at 4.9MB/min with standard settings on Sub-stream.

## Slide 50
Regional Certifications
All documents are MLC portal.
CE
ICASA
FCC
AT&T
Other required certification needs to be actioned by regional office.

## Slide 51
FAQ
How long does it take to load the videos to the UI
Between 5 and 15min after Trip end of OBC events. The Streamax unit is configured with a delay to stay on for 15 minutes after ignition is switched off to allow for the download of videos.
How long are the videos available on UI
We do not have an expiry currently on our server (S3), but we will have to introduce it in the near future to save costs. We may decide to delete videos 1 year and older but currently no limitations in place.
What is the size of the videos
4.9MB/min or 83KB/sec for each camera. A Single event of 8 seconds for 2 cameras is about 1.3MB for SD footage. HD footage estimate is 40MB/min for Road and 20MB/min for InCab camera.
Every time you want to view a video where is it getting the video from
Same as MiX Vision, videos are stored on our S3 server.

## Slide 52
FAQ
Are the videos stored on a server and for how long
As soon as we download the video into our server (S3), we delete it immediately from the Streamax S17 server
and it is then available indefinatly now.
What will the technicians be using to do calibrations
They will be using the "Veyes" app from Streamax in order to calibrate the unit. We will eventually integrate with
SDK into Techtool
Does the Streamax need the ignition wire powered up in order to load the videos to the server
Yes
Is private APN supported
Not in first release

## Slide 53
FAQ
R Watch: Can it include or will include in the future other events notifications such as (Over speeding, Harsh Acceleration, Harsh Cornering ) – Maybe even able to add some customised events ?
No, as it has no knowledge of these OBC events as there is no connection between the two units in the vehicle. The feedback from OBC-triggered events can only be alerted to the driver using the buzzer of the OBC at present.
Like the MiX Vision used to record footage and allows the supervisors to review any footage within the last 72 hours or more depending on the memory capacity. Will this feature still be available and still through MiX Fleet Manager ?
Yes, it is available. Fo 128GB SD card you can access Substream video files for about 90hrs ignition time. Main Stream (HD) is about 20hrs.
Must the vehicle to be online and communicating ?
The MiX Vision AI unit needs to be ON in order to get the video. So if user request a specific video and device is not online, the request will go in a queue and retry later.

## Slide 54
FAQ
What are the limits of the clips – Will it be the same as MiX Vision i.e. a 2 minutes?
Event based video clips are 8 seconds and Tacho (custom clips) 2min 30 sec. Same as current MiX Vision
Will the footage will requested be in HD or possibility to choose resolution output ?
All clips (custom and evidence) are currently in SD. Request HD videos to be added on subsequent release
Any enhancements in these footage (developments or any technology improvements )
Currently the Video Encode standard on the units is set to H264. The supplier is working on H265 which will allow for higher Encoding, resulting in better compression to save data cost.

## Slide 55
Documentation
The following documentation and resources are available on the MiX Learning Centre:
Product Fact Sheet (PFS)
Installation Manual
Cables and Connectors
Certification and Environmental Test Results

## Slide 56
Thank You